## Slide 1: 11 Combined Event
Peter H. Chen

## Slide 2: 11 Combined Event
Combined Event (0:02/4:53)
https://www.learnsystemc.com/basic/event_combined
We discuss the Combined Event. The event can be combined together.
systemC uses wait function to listen to event.
The wait function has different formats accepting the different kind of inputs.
https://www.youtube.com/watch?v=lZiJnihm80o&list=PL2H5BEhPvWMGlFzmCEiUJHH6ZX9VH-i_J&index=11

## Slide 3: 11 Combined Event
Combined Event (0:05/4:53)
https://www.learnsystemc.com/basic/event_combined
The most basic usage of wait() is to provide no input argument.
https://www.youtube.com/watch?v=lZiJnihm80o&list=PL2H5BEhPvWMGlFzmCEiUJHH6ZX9VH-i_J&index=11

## Slide 4: 11 Combined Event
Combined Event (0:10/4:53)
https://www.learnsystemc.com/basic/event_combined
In this case, it will read on the events, that are stated in the sensitivity
We will discuss sensitivity list later.
The second form of wait is to wait for a specific event, e1.
https://www.youtube.com/watch?v=lZiJnihm80o&list=PL2H5BEhPvWMGlFzmCEiUJHH6ZX9VH-i_J&index=11

## Slide 5: 11 Combined Event
Combined Event (0:20/4:53)
https://www.learnsystemc.com/basic/event_combined
It is possible to wait for a list of events.
Here, it waits for event 1, event 2, or event 3.
https://www.youtube.com/watch?v=lZiJnihm80o&list=PL2H5BEhPvWMGlFzmCEiUJHH6ZX9VH-i_J&index=11

## Slide 6: 11 Combined Event
Combined Event (0:30/4:53)
https://www.learnsystemc.com/basic/event_combined
Here, it waits for event 1, event 2, and event 3.
Here, the wait function specify event 1, 2, and 3. All event happens and triggered the process.
https://www.youtube.com/watch?v=lZiJnihm80o&list=PL2H5BEhPvWMGlFzmCEiUJHH6ZX9VH-i_J&index=11

## Slide 7: 11 Combined Event
Combined Event (1:00/4:53)
https://www.learnsystemc.com/basic/event_combined
It is also possible to wait for certain amount of time for that we can provide the time duration into the arguments list of the wait function.
Here, we wait for 200 NS.
https://www.youtube.com/watch?v=lZiJnihm80o&list=PL2H5BEhPvWMGlFzmCEiUJHH6ZX9VH-i_J&index=11

## Slide 8: 11 Combined Event
Combined Event (1:14/4:53)
https://www.learnsystemc.com/basic/event_combined
Furthermore, the time and the event triggers can be combined together.
In this case, it will wait for event e1 or 200 nanoseconds, whichever comes first.
https://www.youtube.com/watch?v=lZiJnihm80o&list=PL2H5BEhPvWMGlFzmCEiUJHH6ZX9VH-i_J&index=11

## Slide 9: 11 Combined Event
Combined Event (1:24/4:53)
https://www.learnsystemc.com/basic/event_combined
Next example shows, we can wait for a certain time and a list of events where we can use logic AND or logic OR for the event list.
https://www.youtube.com/watch?v=lZiJnihm80o&list=PL2H5BEhPvWMGlFzmCEiUJHH6ZX9VH-i_J&index=11

## Slide 10: 11 Combined Event
Combined Event (1:33/4:53)
https://www.learnsystemc.com/basic/event_combined
Cases 9 to 12 are basically, same as cases 5 to 8.
The only differences is instead of passing the double value and the unit separately.
We combine these two into a sc_time object.
https://www.youtube.com/watch?v=lZiJnihm80o&list=PL2H5BEhPvWMGlFzmCEiUJHH6ZX9VH-i_J&index=11

## Slide 11: 11 Combined Event
Combined Event (1:40/4:53)
https://www.learnsystemc.com/basic/event_combined
The last three cases are waiting for clock cycles.
Case 13 does not specify the time unit. The time unit become the clock cycle. Case 13 is 200 clock cycles. Here, we can use for SC_CTHREAD only.
https://www.youtube.com/watch?v=lZiJnihm80o&list=PL2H5BEhPvWMGlFzmCEiUJHH6ZX9VH-i_J&index=11

## Slide 12: 11 Combined Event
Combined Event (1:45/4:53)
https://www.learnsystemc.com/basic/event_combined
The last two cases are wait for one delta cycle. Delta cycle is a direction of zero seconds. It is used to specify the order of execution.
https://www.youtube.com/watch?v=lZiJnihm80o&list=PL2H5BEhPvWMGlFzmCEiUJHH6ZX9VH-i_J&index=11

## Slide 13: 11 Combined Event
Combined Event (1:45/4:53)
https://www.learnsystemc.com/basic/event_combined
Please be aware that a mixture of OR operators and AND operators are not allowed in systemC.
https://www.youtube.com/watch?v=lZiJnihm80o&list=PL2H5BEhPvWMGlFzmCEiUJHH6ZX9VH-i_J&index=11

## Slide 14: 11 Combined Event
Combined Event (2:25/4:53)
https://www.learnsystemc.com/basic/event_combined
We have explained the rules. Let’s take a look at some examples.
https://www.youtube.com/watch?v=lZiJnihm80o&list=PL2H5BEhPvWMGlFzmCEiUJHH6ZX9VH-i_J&index=11

## Slide 15: 11.1 Explain Code

## Slide 16: 11.1 Explain Code
Explain Code (3:00/4:53)
https://www.learnsystemc.com/basic/event_combined
https://www.youtube.com/watch?v=lZiJnihm80o&list=PL2H5BEhPvWMGlFzmCEiUJHH6ZX9VH-i_J&index=11
Within the COMBINED module, we declared a set of events.
Event e1, e2, all the way up to e10.
Then we register trigger thread and several catcher threads surround.

## Slide 17: 11.1 Explain Code
Explain Code (3:00/4:53)
https://www.learnsystemc.com/basic/event_combined
https://www.youtube.com/watch?v=lZiJnihm80o&list=PL2H5BEhPvWMGlFzmCEiUJHH6ZX9VH-i_J&index=11
Within the trigger thread, we fire the different events at different time.
For example, e1 is fired at 1 second, e2 is fired at 2 second, and so on and so forth.
Finally, e10 is fired at 10 second after simulation starts.

## Slide 18: 11.1 Explain Code
Explain Code (3:00/4:53)
https://www.learnsystemc.com/basic/event_combined
https://www.youtube.com/watch?v=lZiJnihm80o&list=PL2H5BEhPvWMGlFzmCEiUJHH6ZX9VH-i_J&index=11
The different catcher threads are designed to catch the different events.
Here, the cactcher_0 is time trigger. It gets triggered event at 2 second.
Here, the cactcher_1 catch event e1.
The cactcher_2and3 catch event e2 AND e3 happens.
The cactcher_4and5 catch event e4 OR e5 happens.
The next three catchers are a combination of time and event list.
catcher_timeout_or_6 is for timeout 5 seconds OR event 6.
catcher_timeout_or_7or8 is for 20 seconds timeout with R event 7 OR event 8.
catcher_timeout_or_9and10 is for 20 seconds timeout with event 9 AND event 10.

## Slide 19: 11.2 Run Code Example

## Slide 20: 11.2 Run Code Example
Run Code Example (3:30/4:53)
https://www.learnsystemc.com/basic/event_combined
In design.cpp, add the SC_MODULE into design.cpp.
In testbench.cpp, add #include “design.cpp”
Select Testbench + Design” “C++/SystemC”
Libraries: “SystemC 2.3.3”
Click “Run”
https://www.youtube.com/watch?v=lZiJnihm80o&list=PL2H5BEhPvWMGlFzmCEiUJHH6ZX9VH-i_J&index=11

## Slide 21: 11.2 Run Code Example
Run Code Example (4:00/4:53)
https://www.learnsystemc.com/basic/event_combined
https://www.youtube.com/watch?v=lZiJnihm80o&list=PL2H5BEhPvWMGlFzmCEiUJHH6ZX9VH-i_J&index=11
At time 1, we catch e1.
At time 2, we have 2 seconds timeout.
At time 3, we catch e2 AND e3.
At time 4, we catch e4 OR e5.
At time 5, we have 5 second timeout before catch e6.
At time 7, we have 20 seconds timeout after catch e7 OR e8.
At time 10, we have 20 seconds timeout after catch e9 AND e10.

## Slide 22: End