## Slide 1: 1 SystemC Basics
Peter H. Chen

## Slide 2: 1 SystemC Basics
SystemC Basics (0:37/11:13)
We discuss how to use SystemC to create a design and synthesizer quickly.
SystemC is a high level coding standard for system level design.
We take it slow in the beginning.
Before we start, let’s go through a few things:
First, we assume you have some knowledge about hardware design and have used the hardware description language like Verilog.
https://www.youtube.com/watch?v=NCFxBGLB5xs&list=PLcvQHr8v8MQLj9tCYyOw44X1PLisEsX-J
First, we assume you have some knowledge about hardware design and have used the hardware description language like Verilog.
If you have background in modeling or algorithm development.
That means you know C very well.
But if you are purely a hardware designer and don’t know C.
Do not worry.

## Slide 3: 1 SystemC Basics
SystemC Basics (1:11/11:13)
https://www.youtube.com/watch?v=NCFxBGLB5xs&list=PLcvQHr8v8MQLj9tCYyOw44X1PLisEsX-J
We don’t know SystemC language.
The is because SystemC is not a language at all.
SystemC is actually a library of C++ classes that are written to emulate the behavior of hardware in a way regular C.
These classes can understand concurrency, bit accuracy, and they can advance time sequentially in a simulation.

## Slide 4: 1.1 Get Started

## Slide 5: 1.1 Get Started
Get Started (2:07/11:13)
https://www.youtube.com/watch?v=NCFxBGLB5xs&list=PLcvQHr8v8MQLj9tCYyOw44X1PLisEsX-J
Let’s get started,
Any design you create is going to start with a module that has a name.
Let’s what is this module looks like in SystemC.
First, we need to include the actual SystemC libraries.
We do this in # (pound) include statement Which include the systemc.h header file. That is the top-level file in SystemC.
It means that our module is going to inherit all the operators, functions, and other constructor available in SystemC.
Next, we will discuss our first SystemC keyword SC_MODULE ().
Everything between the () will become real SystemC Module.
One you have module, we want some input ports.
We can declare the input port with sc_in class followed by the name of the port and “;”.
Output port are declared with the sc_out class.

## Slide 6: 1.1 Get Started
Get Started (2:20/11:13)
https://www.youtube.com/watch?v=NCFxBGLB5xs&list=PLcvQHr8v8MQLj9tCYyOw44X1PLisEsX-J
The sc_in and sc_out are called templates.
We can pass arguments through the <> defined the parameters inside the class.
For sc_in and sc_out, this is their data type like integer or fixed point.
We will discuss data type later
But for now, we just use DT macros as a placeholder for the port data type.

## Slide 7: 1.1 Get Started
Get Started (3:00/11:13)
https://www.youtube.com/watch?v=NCFxBGLB5xs&list=PLcvQHr8v8MQLj9tCYyOw44X1PLisEsX-J
Inside the SC_MODULE, there is a keyword “SC_CTOR” stand for SystemC Constructor.
Inside SC_CTOR (and2), we need the same name “and2” as the SC_MODULE (and2).
This is the same concept as C++.
That constructor initialized the internal signals.

## Slide 8: 1.2 Port I/O

## Slide 9: 1.2 Port I/O
Port I/O (3:27/11:13)
https://www.youtube.com/watch?v=NCFxBGLB5xs&list=PLcvQHr8v8MQLj9tCYyOw44X1PLisEsX-J
We have function called .read() to read values the input port sc_in()
We have function called .write() to write output values port sc_out()
For example, we have input port called inp. We can read value by inp.read()
We have output port called outp. We can write value to the port by outp.write (val).

## Slide 10: 1.3 Add A Function

## Slide 11: 1.3 Add A Function
Add A Function (4:30/11:13)
https://www.youtube.com/watch?v=NCFxBGLB5xs&list=PLcvQHr8v8MQLj9tCYyOw44X1PLisEsX-J
We can add a function, we read value from a.read() and b.read().
We then write value by f.write()

## Slide 12: 1.4 Threads

## Slide 13: 1.4 Threads
Threads (4:41/11:13)
https://www.youtube.com/watch?v=NCFxBGLB5xs&list=PLcvQHr8v8MQLj9tCYyOw44X1PLisEsX-J
Threads is a function made to act like the hardware process
Each threads run concurrently. Thread is something C cannot do. C can only run code in sequence.
Hardware (Threads) are sensitive to signals, clock edges, or fixed amounts of simulation time.
Threads are not called by the user, always active.
SystemC supports three kinds of threads.
They are SC_METHOD(), SC_THREAD(), SC_CTHREAD()

## Slide 14: 1.4 Threads
Threads (5:21/11:13)
https://www.youtube.com/watch?v=NCFxBGLB5xs&list=PLcvQHr8v8MQLj9tCYyOw44X1PLisEsX-J
SC_METHOD() are threads that execute exactly once. Every time, they are triggered by sensitive event.
They runs continuously.
They are directly analogous to a Verilog @always block.
SC_METHODs are supported for synthesis and they are useful for combinational logic or small sequential loci like counters that can be done at one clock cycle.

## Slide 15: 1.4 Threads
Threads (5:30/11:13)
https://www.youtube.com/watch?v=NCFxBGLB5xs&list=PLcvQHr8v8MQLj9tCYyOw44X1PLisEsX-J
Something we do not use very much as SC_THREAD().
SC_THREAD() are runs once at the start of simulation, then suspends itself when done.
SC_THREAD(): If you put an infinity loop in them like a while loop that does something at a fixed time rate.
Sort of like a Verilog @initial block.
However, SC_THREADs are not synthesizable.
They are useful in testbenches. We will see them later in the verification.

## Slide 16: 1.4 Threads
Threads (5:40/11:13)
https://www.youtube.com/watch?v=NCFxBGLB5xs&list=PLcvQHr8v8MQLj9tCYyOw44X1PLisEsX-J
SC_CTHREAD(): “C” means clock. SC_CTHREAD() runs continuously.
They only reference to clock edge. They are synthesizable.
They can take one clock cycle or more clock cycles to execute.
This make most useful for high-level design because abstract design styles like FIR (Finite Impulse Response) filter and h.264 algorithm could take hundreds of clock cycles to execute.
We almost use SC_CTHREAD() is almost every designs you build in synthesizer.
h.264 algorithm
FIR (Finite Impulse Response)

## Slide 17: 1.5 Add Sensitivity

## Slide 18: 1.5 Add Sensitivity
Add Sensitivity (6:00/11:13)
https://www.youtube.com/watch?v=NCFxBGLB5xs&list=PLcvQHr8v8MQLj9tCYyOw44X1PLisEsX-J
SC_METOD() is the best method to use for combinational logic.

## Slide 19: 1.5 Add Sensitivity
Add Sensitivity (7:01/11:13)
https://www.youtube.com/watch?v=NCFxBGLB5xs&list=PLcvQHr8v8MQLj9tCYyOw44X1PLisEsX-J
SC_METOD() is the best method to use for combinational logic.

## Slide 20: 1.5 Add Sensitivity
Add Sensitivity (7:22/11:13)
https://www.youtube.com/watch?v=NCFxBGLB5xs&list=PLcvQHr8v8MQLj9tCYyOw44X1PLisEsX-J
We want to sensitive all the input signals.
a and b are lists of signals. The signals are separated by SystemC left shot operator (<<) are overloaded for sensitive signals or events.

## Slide 21: 1.5 Add Sensitivity
Add Sensitivity (7:37/11:13)
What happened to the sequential function?
In other word, sensitive to a rising clock edge. We add another input clock.
https://www.youtube.com/watch?v=NCFxBGLB5xs&list=PLcvQHr8v8MQLj9tCYyOw44X1PLisEsX-J

## Slide 22: 1.5 Add Sensitivity
Add Sensitivity (7:37/11:13)
What happened to the sequential function?
In other word, sensitive to a rising clock edge. We add another input clock.
https://www.youtube.com/watch?v=NCFxBGLB5xs&list=PLcvQHr8v8MQLj9tCYyOw44X1PLisEsX-J

## Slide 23: 1.5 Add Sensitivity
Add Sensitivity (8:24/11:13)
Positive clock and negative clock.
https://www.youtube.com/watch?v=NCFxBGLB5xs&list=PLcvQHr8v8MQLj9tCYyOw44X1PLisEsX-J

## Slide 24: 1.5 Add Sensitivity
Add Sensitivity (8:36/11:13)
Positive clock and negative clock.
https://www.youtube.com/watch?v=NCFxBGLB5xs&list=PLcvQHr8v8MQLj9tCYyOw44X1PLisEsX-J

## Slide 25: 1.6 Data Types

## Slide 26: 1.6 Data Types
Data Types (8:42/11:13)
https://www.youtube.com/watch?v=NCFxBGLB5xs&list=PLcvQHr8v8MQLj9tCYyOw44X1PLisEsX-J
Unsigned Integer
Signed Integer

## Slide 27: 1.6 Data Types
Unsigned Integer (8:42/11:13)
https://www.youtube.com/watch?v=NCFxBGLB5xs&list=PLcvQHr8v8MQLj9tCYyOw44X1PLisEsX-J
Width = 3

## Slide 28: 1.6 Data Types
Signed Integers (9:40/11:13)
https://www.youtube.com/watch?v=NCFxBGLB5xs&list=PLcvQHr8v8MQLj9tCYyOw44X1PLisEsX-J

## Slide 29: 1.6 Data Types
Add Datatypes (9:40/11:13)
We are going to add DT datatype for real SystemC datatype.
https://www.youtube.com/watch?v=NCFxBGLB5xs&list=PLcvQHr8v8MQLj9tCYyOw44X1PLisEsX-J

## Slide 30: 1.6 Data Types
Add Datatypes (9:40/11:13)
For 1 bit unsigned data bit.
https://www.youtube.com/watch?v=NCFxBGLB5xs&list=PLcvQHr8v8MQLj9tCYyOw44X1PLisEsX-J

## Slide 31: 1.7 Review

## Slide 32: 1.7 Review
Review (10:12/11:13)
https://www.youtube.com/watch?v=NCFxBGLB5xs&list=PLcvQHr8v8MQLj9tCYyOw44X1PLisEsX-J
Read in and write port
Construct module that is designate a function to be a thread
Describe a system C module
Add Input/Output Port

## Slide 33: 1.7 Review
Review (10:49/11:13)
https://www.youtube.com/watch?v=NCFxBGLB5xs&list=PLcvQHr8v8MQLj9tCYyOw44X1PLisEsX-J
Different kinds of thread SC Methods.
We made the thread sensitive to signal or clock edges using the sensitive keyword with the left shift operator and learn about
clk.pos and clk.neg for clock edge functions and

## Slide 34: 1.7 Review
Review (10:55/11:13)
https://www.youtube.com/watch?v=NCFxBGLB5xs&list=PLcvQHr8v8MQLj9tCYyOw44X1PLisEsX-J
We introduced to system C integer data type sc_uint for unsigned and sc_int for signed.

## Slide 35: End