## Slide 1: 6 Simulation Process
Peter H. Chen

## Slide 2: 6 Simulation Process
Simulation Process (0:02/4:06)
https://www.learnsystemc.com/basic/simu_process
A simulation Process is a member function of sc_module class
A simulation process has no input arguments and no return values
A simulation process is registered with the simulation kernel and let the simulation kernel trigger those simulation processes.
https://www.youtube.com/watch?v=vhGnMNJO3WI&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=6

## Slide 3: 6 Simulation Process
Simulation Process (0:02/4:06)
https://www.learnsystemc.com/basic/simu_process
There are three different kind of simulation processes supported by systemC.
1. One is SC_METHOD() which does not have its own thread of execution. It contains no simulation time. It cannot be suspended and you cannot call the code again upon wait().
2. Another simulation process is SC_THREAD() which has its own thread of execution. It may consume simulated time. It can be suspended. And the code can be called again upon wait.
3. The last one is SC_CTHREAD(), i.e., systemC clock thread, which is a special form of SC_THREAD(). It has only one static sensitivity which is a clock edge event.
Even though those three different simulation processes are supported by systemC, one of them is most important which is SC_THREAD() because it can do everything that SC_METHOD or SC_CTHREAD() does.
In order for SC_THREAD() or SC_CTHREAD() processes to be called again, there should be a while loop.
https://www.youtube.com/watch?v=vhGnMNJO3WI&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=6

## Slide 4: 6 Simulation Process
Simulation Process (0:02/4:06)
https://www.learnsystemc.com/basic/simu_process
The SC_METHOD() process is different. SC_METHOD() does not require a while loop and is invoked again by calling the next trigger method.
For SC_THREAD or SC_CTHREAD(), it may consume some simulating time to finish.
Please be aware the simulated time in the systemC is not the extra time that the program runs.
The simulation time is just a counter. It is a counter managed by the simulation kernel.
We will discuss the concept simulated time in later session.
https://www.youtube.com/watch?v=vhGnMNJO3WI&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=6

## Slide 5: 6.1 Code Example

## Slide 6: 6.1 Code Example
Code Example (2:00/4:06)
https://www.learnsystemc.com/basic/simu_process
https://www.youtube.com/watch?v=vhGnMNJO3WI&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=6
First, we define a SC_MODULE. The module name is “PROCESS”.
Inside this SC_MODULE, there are three different simulation processes.
1. One is method function, registered to the simulation kernel using the SC_METHOD().
2. Another one is thread function, register to the simulation kernel using the SC_THREAD().
3. The last one is a cthread function, which is registered as SC_CTHREAD().

## Slide 7: 6.1 Code Example
Code Example (2:00/4:06)
https://www.learnsystemc.com/basic/simu_process
https://www.youtube.com/watch?v=vhGnMNJO3WI&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=6
In the three different simulation processes, it print the message when the simulation process is invoked.

## Slide 8: 6.1 Code Example
Code Example (2:00/4:06)
https://www.learnsystemc.com/basic/simu_process
https://www.youtube.com/watch?v=vhGnMNJO3WI&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=6
We also see here:
In order for the message process to be invoked again, we use the next triggered method.
Here, we asked the simulation kernel to trigger the method process after one second.

## Slide 9: 6.1 Code Example
Code Example (2:00/4:06)
https://www.learnsystemc.com/basic/simu_process
https://www.youtube.com/watch?v=vhGnMNJO3WI&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=6
For a thread, as discussed earlier, we have to define a while loop.
Within the while loop, we print some message and wait 1 second before it is triggered again.

## Slide 10: 6.1 Code Example
Code Example (2:00/4:06)
https://www.learnsystemc.com/basic/simu_process
https://www.youtube.com/watch?v=vhGnMNJO3WI&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=6
cthread, as shown here, is triggered based on the input clock.
Where is clock is defined as a trigger which is defined in second.

## Slide 11: 6.1 Code Example
Code Example (2:00/4:06)
https://www.learnsystemc.com/basic/simu_process
https://www.youtube.com/watch?v=vhGnMNJO3WI&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=6
The simulation processes is triggered in every second in the main function.
We declare the process object of PROCESS module.
Then, we start the systemC to run for 2 seconds before it finished.

## Slide 12: 6.2 Run Code Example

## Slide 13: 6.2 Run Code Example
Run Code Example (3:46/4:06)
https://www.learnsystemc.com/basic/module
Copy the code example into EDA playground.
Select C++/SystemC testbench + Design
Select SystemC 2.3.3 Libraries
Click “Run”
https://www.youtube.com/watch?v=vhGnMNJO3WI&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=6

## Slide 14: 6.2 Run Code Example
Run Code Example (3:46/4:06)
https://www.learnsystemc.com/basic/module
When we run for 2 seconds, we can see the method process is triggered twice at time zero and time one.
The thread and cthread processes are also triggered twice at time zero and time one but they use different ways to be triggered.
https://www.youtube.com/watch?v=vhGnMNJO3WI&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=6

## Slide 15: End