## Slide 1: 7 Simulation Stage
Peter H. Chen

## Slide 2: 7 Simulation Stage
Simulation Process (0:02/3:58)
https://www.learnsystemc.com/
https://www.learnsystemc.com/basic/simu_stage
We discuss the different stages if system C.
https://www.youtube.com/watch?v=gQZiPwBAAoI&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=7

## Slide 3: 7 Simulation Stage
Simulation Process (0:02/3:58)
https://www.learnsystemc.com/
https://www.learnsystemc.com/basic/simu_stage
As shown in the below diagram, there are three different stages: an elaboration stage, a clean up stage, and execution stage.
The three different stages are separated by sc_start() function.
https://www.youtube.com/watch?v=gQZiPwBAAoI&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=7

## Slide 4: 7 Simulation Stage
Simulation Process (0:24/3:58)
https://www.learnsystemc.com/
After sc_start is cleanup.
Upon encountering sc_start(), systemC simulation kernel will take over the charge and it enters the execution stage which is further divided into tow sub-stages: initialization stage and simulation stage.
https://www.youtube.com/watch?v=gQZiPwBAAoI&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=7

## Slide 5: 7 Simulation Stage
Simulation Process (0:41/3:58)
https://www.learnsystemc.com/
Initialization stage happens in the very beginning to initialize the systemc modules to do the port binding and etc.
Within the simulation stage, it has three different sub-steps: An evaluation step, an Update step, and step to advance time.
Evaluation step is where the systemC simulation kernel will trigger different simulation processes run some statements.
https://www.youtube.com/watch?v=gQZiPwBAAoI&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=7

## Slide 6: 7 Simulation Stage
Simulation Process (1:04/3:58)
https://www.learnsystemc.com/
Afterwards, it will update the value and will check if there are pending simulation processes in the future.
If yes, it will advance the time to execute the next simulation process, otherwise, it will end the execution phase.
Upon returning from sc_start(), we enter the cleanup stage, which can do some post-processing cleanup, for example, close file, open file, and etc. and this is the end of the program.
https://www.youtube.com/watch?v=gQZiPwBAAoI&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=7

## Slide 7: 7 Simulation Stage
Simulation Process (1:04/3:58)
https://www.learnsystemc.com/basic/simu_stage
Let’s look at an example of simulation stages.
https://www.youtube.com/watch?v=gQZiPwBAAoI&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=7

## Slide 8: 7 Simulation Stage
Simulation Process (1:04/3:58)
https://www.learnsystemc.com/basic/simu_stage
Let’s look at an example of simulation stages.
https://www.youtube.com/watch?v=gQZiPwBAAoI&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=7

## Slide 9: 7 Simulation Stage
Simulation Process (1:04/3:58)
https://www.learnsystemc.com/basic/simu_stage
By the way, we have four callback function which are called by the simulation kernel at different stages and where you can have your own code inserted. Those functions are listed below.
1. The first one is called before_end_of_elaboration(): It is called after the construction of the modal hierarchy.
2. The second one is called end_of_elaboration(): This is called at the very end of the elaboration phase.
3. The third one is called at the start_of_simulation():
4. The last one is called end_of_simulation(): Finished the simulation.
https://www.youtube.com/watch?v=gQZiPwBAAoI&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=7

## Slide 10: 7.1 Code Example

## Slide 11: 7.1 Code Example
Code Example (2:00/3:58)
https://www.learnsystemc.com/basic/simu_stage
https://www.youtube.com/watch?v=gQZiPwBAAoI&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=7
First, we define a SC_MODULE.
The stage module has a constructor which is called during the elaboration phase.
It will print a “Elaboration: constructor” message.
We also define a destructor function ~STAGE() which is called during the cleanup stage.
The module also has a thread which is registered to the simulator kernel using SC_THREAD().

## Slide 12: 7.1 Code Example
Code Example (2:00/3:58)
https://www.learnsystemc.com/basic/simu_stage
https://www.youtube.com/watch?v=gQZiPwBAAoI&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=7
Within the thread() method, there are two portions of code:
1. One is called during the initialization stage.
2. The other one is while loop which is called at runtime during the simulation stage.
Within the thread method, we also insert an sc_stop() function.
The purpose of this line is to end the simulation after two iterations.

## Slide 13: 7.1 Code Example
Code Example (2:00/3:58)
https://www.learnsystemc.com/basic/simu_stage
https://www.youtube.com/watch?v=gQZiPwBAAoI&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=7
Here, we also customize the four callback functions.
1. before_end_of_elaboration()
2. end_of_elaboration()
3. start_of_simulation()
4. end_of_simulation()

## Slide 14: 7.1 Code Example
Code Example (2:00/3:58)
https://www.learnsystemc.com/basic/simu_stage
https://www.youtube.com/watch?v=gQZiPwBAAoI&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=7
In sc_main() function, we first to create an object of STAGE class.
Afterward, we give the control to systemC simulation kernel.
The simulation finished when sc_stop() return.

## Slide 15: 7.2 Run Code Example

## Slide 16: 7.2 Run Code Example
Run Code Example (3:46/4:06)
https://www.learnsystemc.com/basic/module
Copy the code example into EDA playground.
Select C++/SystemC testbench + Design
Select SystemC 2.3.3 Libraries
Click “Run”
https://www.youtube.com/watch?v=gQZiPwBAAoI&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=7

## Slide 17: 7.2 Run Code Example
Run Code Example (3:46/4:06)
https://www.learnsystemc.com/basic/module
https://www.youtube.com/watch?v=gQZiPwBAAoI&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=7
When running the example, we have the following results below:
1. We first enter the elaboration stage at time 0 where all the constructors are called.
2. Afterwards are tow callback functions before end of elaboration.
After elaboration stage is a simulation stage.
1. First, the simulation kernel triggers the callback function, start_of_simulation()
2. Afterwards, it enter the initialization stage, after initialization, the systemC simulations runs.
Within this stage, the simulation processes are called repeatedly until it stops and
3. Simulation kernels calls the end_of_simulation()
Finally, destructor functions are called during the cleanup stage. And the program returns.

## Slide 18: End