## Slide 1: 10 Event
Peter H. Chen

## Slide 2: 10 Event
Concurrency (0:02/3:07)
https://www.learnsystemc.com/basic/event
We discuss the Event of systemC.
We will synchronize the activities among the concurrent processes.
This synchronization is achieved using event.
https://www.youtube.com/watch?v=vysRn1WYqtw&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=10

## Slide 3: 10 Event
Concurrency (0:12/3:07)
https://www.learnsystemc.com/basic/event
The event is an object of class, sc_event.
It is used for the purpose of synchronization.
https://www.youtube.com/watch?v=vysRn1WYqtw&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=10

## Slide 4: 10 Event
Concurrency (0:20/3:07)
https://www.learnsystemc.com/basic/event
An event has the following methods:
1. First method is notify(). it can generate an immediate notification.
2. Second method is generate notification after certain time.
3. The third method is used to cancel a pending notification.
https://www.youtube.com/watch?v=vysRn1WYqtw&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=10

## Slide 5: 10 Event
Concurrency (0:30/3:07)
https://www.learnsystemc.com/basic/event
Please be aware immediate notification cannot be cancelled.
There can be at most one pending notification for any give event what it means is if you have an event and the notification time is two seconds later, then you trigger the event again with notification time of one second.
It will only generate one notification after one second and the other notification is cancelled.
https://www.youtube.com/watch?v=vysRn1WYqtw&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=10

## Slide 6: 10.1 Run Code Example

## Slide 7: 10.1 Run Code Example
Run Code Example (1:22/3:07)
https://www.learnsystemc.com/basic/event
Select Testbench + Design” “C++/SystemC”
Libraries: “SystemC 2.3.3”
Click “Run”
https://www.youtube.com/watch?v=vysRn1WYqtw&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=10

## Slide 8: 10.1 Run Code Example
Run Code Example (1:30/3:07)
https://www.learnsystemc.com/basic/event
https://www.youtube.com/watch?v=vysRn1WYqtw&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=10
We define a model with two threads.
A trigger thread and a catcher thread.
We also declare an event to synchronize the activities between the trigger thread and catcher thread.
Within the trigger thread, every two seconds, it generates a notification. The notification will be triggered after 1 second.
Within the catcher thread, it listens to the event with wait (e), it print “Event catch at ..”, when the event is received.

## Slide 9: 10.1 Run Code Example
Run Code Example (1:30/3:07)
https://www.learnsystemc.com/basic/event
https://www.youtube.com/watch?v=vysRn1WYqtw&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=10
After time = 4 seconds, we cancel the event and then wait for 2 seconds.

## Slide 10: 10.1 Run Code Example
Run Code Example (1:50/3:07)
https://www.learnsystemc.com/basic/event
https://www.youtube.com/watch?v=vysRn1WYqtw&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=10
We set the simulation time is 8 seconds.

## Slide 11: 10.2 Result

## Slide 12: 10.2 Result
Result (2:00/3:07)
https://www.learnsystemc.com/basic/event
https://www.youtube.com/watch?v=vysRn1WYqtw&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=10
After 1 second, we trigger the event, the catcher thread catch the event and print “Event catch message”. (time = 1 second)
We wait 2 seconds and catch the event (time = 3 second).
We cancel the event at 4 second.
And then we wait for 2 second which is time = 6 second.
We wait 1 second (time = 7 second), then, we trigger another event at 7 seconds.

## Slide 13: 10.3 Debugger

## Slide 14: 10.3 Debugger
Debugger (2:30/3:07)
https://www.learnsystemc.com/basic/event
https://www.youtube.com/watch?v=vysRn1WYqtw&list=PL1qVKHVG3ZfVb91esBQ0-0SQC3dGGeXkn&index=10
Set break point in trigger thread and catcher thread.

## Slide 15: End