## Slide 1: 1 SystemC
Peter H. Chen

## Slide 2: 1 SystemC
SystemC
SystemC is a set of C++ classes and macros which provide an event-driven simulation interface (see also discrete event simulation).
These facilities enable a designer to simulate concurrent processes, each described using plain C++ syntax.
SystemC processes can communicate in a simulated real-time environment, using signals of all the datatypes offered by C++, some additional ones offered by the SystemC library, as well as user defined. In certain respects, SystemC deliberately mimics the hardware description languages VHDL and Verilog, but is more aptly described as a system-level modeling language.
SystemC is applied to system-level modeling, architectural exploration, performance modeling, software development, functional verification, and high-level synthesis.
SystemC is often associated with electronic system-level (ESL) design, and with transaction-level modeling (TLM).
Compared to HDLs
SystemC has semantic similarities to VHDL and Verilog, but may be said to have a syntactical overhead compared to these when used as a hardware description language.
On the other hand, it offers a greater range of expression, similar to object-oriented design partitioning and template classes.
Although strictly a C++ class library, SystemC is sometimes viewed as being a language in its own right.
Source code can be compiled with the SystemC library (which includes a simulation kernel) to give an executable.
The performance of the OSCI open-source implementation is typically less optimal than commercial VHDL/Verilog simulators when used for register transfer level simulation.
https://www.youtube.com/watch?v=7Yd_xa8l76g&list=PLv4ReNnZeDivIoS5Pjc8HK6MHMy4V4LpO
We discuss how to simulate C++ and SystemC Library on EDA playground.
SystemC is a Library for system-level simulations and it includes the simulation kernel which allows you to have a concept of time

## Slide 3: 1.1 EDA Playground for SystemC

## Slide 4: 1.1 EDA Playground for SystemC
EDA Playground for SystemC
We go to EDA Playground:
https://www.edaplayground.com/
We select the “C++/SystemC” for language here.
https://www.youtube.com/watch?v=7Yd_xa8l76g&list=PLv4ReNnZeDivIoS5Pjc8HK6MHMy4V4LpO

## Slide 5: 1.1 EDA Playground for SystemC
EDA Playground for SystemC
Then we select couple of example here.
We select C++/SystemC.
https://www.youtube.com/watch?v=7Yd_xa8l76g&list=PLv4ReNnZeDivIoS5Pjc8HK6MHMy4V4LpO

## Slide 6: 1.1 EDA Playground for SystemC
EDA Playground for SystemC
We select the simple Counter.
https://www.youtube.com/watch?v=7Yd_xa8l76g&list=PLv4ReNnZeDivIoS5Pjc8HK6MHMy4V4LpO

## Slide 7: 1.1 EDA Playground for SystemC
EDA Playground for SystemC
We select the system C2.3.3
https://www.youtube.com/watch?v=7Yd_xa8l76g&list=PLv4ReNnZeDivIoS5Pjc8HK6MHMy4V4LpO

## Slide 8: 1.1 EDA Playground for SystemC
EDA Playground for SystemC
Click Run.
https://www.youtube.com/watch?v=7Yd_xa8l76g&list=PLv4ReNnZeDivIoS5Pjc8HK6MHMy4V4LpO

## Slide 9: 1.1 EDA Playground for SystemC
EDA Playground for SystemC
You can see the simulation in Log area.
https://www.youtube.com/watch?v=7Yd_xa8l76g&list=PLv4ReNnZeDivIoS5Pjc8HK6MHMy4V4LpO

## Slide 10: 1.1 EDA Playground for SystemC
EDA Playground for SystemC
In the left testbench which we toggle some of the signals, like, assert, reset, enable, and etc.
https://www.youtube.com/watch?v=7Yd_xa8l76g&list=PLv4ReNnZeDivIoS5Pjc8HK6MHMy4V4LpO

## Slide 11: 1.1 EDA Playground for SystemC
EDA Playground for SystemC
In the tools & Simulators section, we select the “open EPWave after run”.
https://www.youtube.com/watch?v=7Yd_xa8l76g&list=PLv4ReNnZeDivIoS5Pjc8HK6MHMy4V4LpO

## Slide 12: 1.1 EDA Playground for SystemC
EDA Playground for SystemC
By default, SystemC will dump the wave.
You can see the SystemC is running on the Server.
We have the following output.
We can see the reset and enable are inserted and counter started to counting.
https://www.youtube.com/watch?v=7Yd_xa8l76g&list=PLv4ReNnZeDivIoS5Pjc8HK6MHMy4V4LpO

## Slide 13: 1.1 EDA Playground for SystemC
EDA Playground for SystemC
We can rerun with compile option “-v”.
This will show the verbose information of run.
https://www.youtube.com/watch?v=7Yd_xa8l76g&list=PLv4ReNnZeDivIoS5Pjc8HK6MHMy4V4LpO

## Slide 14: End